Directions for Use of the Hazard Analysis Form

- Make sure that every step shown on the Process Flow Diagram is entered in the Hazard Analysis Form.  Make sure that each step has the same name and number in both the Process Flow Diagram and the Hazard Analysis Form.

- Check the three categories of hazard (Biological, Chemical, Physical) shown for each step.

  - If you think a listed hazard is not reasonably likely to occur, leave it in column 2 (Food Safety Hazard) and enter “No” in column 3 (Reasonably likely to occur?).  Then provide a reason in column 4.

  - If you think there are no relevant hazards for a particular category, delete the listed hazard and write “none” in column 2, write “No” in column 3, provide a reason in column 4, and cross out any information in columns 5 – 6.

  - If you think that a relevant hazard should be added at a step, describe the hazard in column 2 (Food Safety Hazard).  Then determine whether the hazard is reasonably likely to occur and put the answer in column 3.  Then provide, in column 4, a reason for deciding whether or not the hazard is reasonably likely to occur.

    - For example, following an SSOP, SOP, or approved formulation may make a hazard unlikely to occur, or a supplier may provide a letter of guarantee stating that the hazard should not be present.

    - On the other hand, a history of outbreaks or contamination related to a hazard would mean that the hazard IS reasonably likely to occur.

Columns 5 and 6 can be left blank if a hazard is NOT reasonably likely to occur.

IF the hazard IS reasonably likely to occur: fill in columns 5 and 6.

- In column 5, list measures that could be applied to prevent, eliminate, or reduce the hazard to an acceptable level.  NOTE: at least one of these measures must be either a Critical Control Point (CCP) at the present step or a CCP at a later step.

  - Finally, if the hazard is controlled by a CCP at the present step, enter the CCP number in the 6th column.  The accepted numbering system is to number the CCP’s in order, followed by either B, C, or P to indicate what type of hazard is being controlled.  For example, if the 2nd CCP in a process controlled a physical hazard, it would be entered as CCP -2P.

  - I f you agree that a listed hazard is relevant, no changes are necessary.

HAZARD ANALYSIS – HEAT TREATED, SHELF STABLE – Snack Sticks, Summer Sausage, Jerky

| 1. Process Step | 2. Food Safety Hazard | 3. Reasonably likely to occur? | 4. Basis of decision for whether reasonably likely to occur | 5. If Yes in Column 3, What Measures Could be Applied to Prevent, Eliminate, or Reduce the Hazard to an Acceptable Level? | 6. Critical Control Point |
| --- | --- | --- | --- | --- | --- |
| 1. Receiving Packaging Materials | Biological – Contamination with meat, other biological material | No | SOP for receiving makes hazard unlikely to occur. |  |  |
|  | Chemical – Non-food grade materials | No | Letter of guarantee for packaging materials makes hazard unlikely to occur. |  |  |
|  | Physical - None | No | SOP for receiving makes hazard unlikely to occur. |  |  |
| 2. Receiving Raw Meat/Poultry, natural casings, starter cultures | Biological - Presence of pathogens: Salmonella, Listeria monocytogenes, Staph. aureus, Clostridium botulinum, Clostridium perfringens; if beef E. coli 0157:H7; if poultry, Campylobacter Presence of BSE-causing prions in beef casings | Yes (Pathogens) No (Prions) | Raw meat/poultry, natural casings are known sources of pathogens Letter of guarantee received from all suppliers of natural beef casings to certify that casings are not obtained from SRMs. | Pathogens will be controlled at subsequent steps through heat treatment and drying (jerky & snack sticks) or fermentation/ acidification and heating (summer sausage, snack stick). |  |
|  | Chemical – None | No | SOP for receiving makes hazard unlikely to occur. |  |  |
|  | Physical – None | No | SOP for receiving makes hazard unlikely to occur. |  |  |
| 3. Receiving and 6. Storage– Restricted and Unrestricted Non-meat\Non-poultry Food Ingredients | Biological – None | No | SOP for receiving and storage makes hazard unlikely to occur. |  |  |
|  | Chemical – Ingredients containing undesirable substances | No | Letters of guarantee are received from all suppliers of food additives. SOP for storage makes contamination unlikely. |  |  |
|  | Physical – None | No | SOP for receiving makes hazard unlikely to occur. |  |  |
| 4. Storage (Cold – Frozen/Refrigerated) – Raw Meat/Poultry, natural casings, starter culture | Biological: Presence or growth of pathogens (see list above) | Yes (Presence) No (growth) | Raw meat/poultry, natural casings are known sources of pathogens. Pathogens are not likely to grow if the product is maintained according to the SOP for storage. | Pathogens will be controlled at subsequent steps through heat treatment and drying (jerky & snack sticks) or fermentation/ acidification and heating (summer sausage, snack stick). |  |
|  | Chemical – None | No | SOP for storage makes hazard unlikely to occur. |  |  |
|  | Physical – None | No | SOP for receiving makes hazard unlikely to occur. |  |  |
| 5. Tempering Frozen Meat/Poultry | Biological – Presence or growth of pathogens (see list above) | Yes (presence) No (growth) | Raw meat/poultry are known sources of pathogens. Tempering done according to SOP, therefore pathogen growth is unlikely. | Pathogens will be controlled at subsequent steps through heat treatment and drying (jerky & snack sticks) or fermentation/acidification and heating (summer sausage, snack stick). |  |
|  | Chemical – None | No | SSOP makes hazard unlikely to occur. |  |  |
|  | Physical - None | No | SSOP makes hazard unlikely to occur. |  |  |
| 7. Weighing Raw Meat/Poultry | Biological – Presence or growth of pathogens (see list above) | Yes (presence) No (growth) | Raw meat/poultry are known sources of pathogens. Weighing done quickly enough to prevent growth. SSOP makes contamination via equipment and workers unlikely to occur. | Pathogens will be controlled at subsequent steps through heat treatment and drying (jerky & snack sticks) or fermentation/acidification and heating (summer sausage, snack stick). |  |
|  | Chemical – None | No | SSOP makes hazard unlikely to occur. |  |  |
|  | Physical – None | No | SSOP makes hazard unlikely to occur. |  |  |
| 8.Weighing Restricted and Unrestricted Non-meat/Non-poultry Food Ingredients | Biological – None | No | SSOP (operational) makes hazard unlikely to occur. |  |  |
|  | Chemical – Excessive Level of Nitrite | No | Approved product formulation will be followed to prevent addition of too much nitrite. Use of pre-blended cure mixes added to standardized amounts of meat makes hazard unlikely to occur. |  |  |
|  | Physical - None | No | SSOP makes hazard unlikely to occur. |  |  |
| 9. Combining Ingredients, and Forming/Shaping Product (Includes one or more of the following; grinding, mixing, adding starter culture, marinating, stuffing, forming, and slicing) | Biological – Presence or growth of pathogens (see list above) | Yes (presence) No (growth) | Raw meat/poultry, natural casings are known sources of pathogens. Processing steps are done quickly enough to prevent growth. SSOP makes contamination via equipment and workers unlikely to occur. | Pathogens will be controlled at subsequent steps through heat treatment and drying (jerky & snack sticks) or fermentation/acidification and heating (summer sausage, snack stick). Spore-forming pathogens will not be able to grow on finished product (products are shelf-stable). |  |
|  | Chemical – Allergens; cleaning/sanitizing chemical residues | No | Application of correct label prevents inadvertent consumption of allergens by consumer. Operational SSOP prevents cross contamination of allergenic agents. Pre-op SSOP makes presence of chemical residues unlikely to occur. |  |  |
|  | Physical – Foreign materials | No | Visual observation for foreign materials during processing, inspection of equipment during cleaning make hazard unlikely. |  |  |
| 17. Storage of packaging materials, incl. collagen or synthetic casings | Biological – contamination from meat products | No | SOP for receiving and storage makes hazard unlikely |  |  |
|  | Chemical – None | No | SOP for receiving and storage makes hazard unlikely |  |  |
|  | Physical - None | No | SOP for receiving and storage makes hazard unlikely |  |  |
| 10. Racking/Hanging | Biological – Presence or growth of pathogens (see list above) | Yes (Presence) No (Growth) | Raw meat/poultry, natural casings are a known source of pathogens. Process is done rapidly enough to prevent growth, and product is returned to cooler if not promptly fermented or heat-processed. SSOP makes contamination via equipment & workers unlikely to occur. | Pathogens will be controlled at a subsequent step through heat treatment and drying (jerky & snack sticks) and/or fermentation or acidification and heating (summer sausage, snack stick). |  |
|  | Chemical – None | No | SOP for storage makes hazard unlikely to occur. |  |  |
|  | Physical - None | No | SOP for storage makes hazard unlikely to occur. |  |  |
| 11. Fermenting (Used for pH reduction of Snack Sticks, Summer Sausage, Landjaeger) | Biological – Presence or growth of pathogens (see list in step 2) | Yes (S. aureus) No (other pathogens) | Potential growth of Staphylococcus aureus and toxigenesis if fermentation process is inadequate. Growth of other non-sporeforming pathogens may occur, but hazard is controlled by subsequent heat-processing. | Fermentation within the degree- hour limit will achieve the pH needed to inhibit S. aureus. Spore-forming pathogens will not be able to grow on finished product (products are shelf-stable). In some cases, decrease in pH to less than 5.3 is required for shelf-stability. | 1 B |
|  | Chemical – None | No | SSOP makes hazard unlikely to occur. |  |  |
|  | Physical - None | No | SSOP makes hazard unlikely to occur. |  |  |
| 12. Heat Treatment (Cooking Step) 13. Drying | Biological – Pre-process contaminating pathogens: Listeria monocytogenes Salmonella, Staphylococcus aureus, E. coli 0157:H7 , Clostridium botulinum, Clostridium perfringens | Yes | Potential survival and growth of pre-processing contaminating pathogens and toxin production by S. aureus due to inadequate process time/temperature/% relative humidity. | Heat treatment using appropriate time/temperature/humidity to produce lethality/pasteurization. | 2 B |
|  | Chemical – None | No | SSOP makes hazard unlikely to occur. |  |  |
|  | Physical - None | No | SSOP makes hazard unlikely to occur. |  |  |
|  | Biological - Post-process contaminating pathogens: Listeria monocytogenes, Staphylococcus aureus, toxin-producing molds | Yes (bacteria) No (molds) | Spore-forming pathogens may survive. Post-process contamination may occur. SOP for oxygen-free packaging and/or discarding of moldy product makes hazard unlikely. | Product will be dried to an extent that prevents growth of sporeforming bacterial pathogens. For some shelf-stable products, reduced pH and reduced water activity combine to prevent growth of bacterial pathogens. | 3B |
|  | Chemical – None | No | SSOP makes hazard unlikely. |  |  |
|  | Physical - None | No | SSOP makes hazard unlikely. |  |  |
| 14. Short-term storage | Biological – Growth of Listeria monocytogenes, Staphylococcus aureus, toxin-producing molds | No | Short duration of step and reduced water activity make growth unlikely to occur. Spore-forming pathogens will not grow because products are shelf-stable. |  |  |
|  | Chemical – None | No | SSOP makes hazard unlikely. |  |  |
|  | Physical - None | No | SSOP makes hazard unlikely. |  |  |
| 15. Slicing or cutting finished product | Biological – Contamination with pathogens via workers or equipment. Growth of Listeria monocytogenes, Staphylococcus aureus. Growth of toxin-producing molds | No No No | SSOP controls hygienic condition of equipment and practices of employees handling products in post-lethality environment. Short duration of step makes growth unlikely. Drying prevents pathogen growth. Listeria control program is in effect. Short duration of step makes growth unlikely. SOP for oxygen-free packaging and/or discarding of moldy product makes mold growth unlikely. |  |  |
|  | Chemical – None | No | SSOP makes hazard unlikely. |  |  |
|  | Physical - None | No | SSOP makes hazard unlikely. |  |  |
| 16. Spraying w/ potassium sorbate | Biological – None | No | Potassium sorbate is an approved antimicrobial agent. |  |  |
|  | Chemical – excessive potassium sorbate | No | Applying potassium sorbate according to approved formulation makes hazard unlikely to occur |  |  |
|  | Physical - None | No | SSOP makes hazard unlikely. |  |  |
| 18. Packaging/Labeling | Biological - Growth of Listeria monocytogenes, Staphylococcus aureus Growth of toxin-producing molds | No No | Product is shelf-stable and does not permit growth of bacterial pathogens. Listeria control program. SOP for oxygen-free packaging and/or discarding of moldy product makes hazard unlikely. |  |  |
|  | Chemical – None | No | SSOP makes hazard unlikely. |  |  |
|  | Physical - None | No | SSOP makes hazard unlikely. |  |  |
| 19. Finished Product Storage | Biological – None | No | Product is shelf-stable. |  |  |
|  | Chemical – None | No | Product is handled according to SOP for Finished Product Storage. |  |  |
|  | Physical - None | No | Product is handled according to SOP for Finished Product Storage. |  |  |
| 20. Shipping or Retail | Biological – None | No | Product is shelf-stable. |  |  |
|  | Chemical – None | No | Product is handled according to SOP for Finished Product Storage. |  |  |
|  | Physical - None | No | Product is handled according to SOP for Finished Product Storage. |  |  |